Cheat sheet – Connection PADDLE 2.0

Connections BBB:
P8_36	ePWMSS1A	PWM Motor 1
P8_45	ePWMSS2A	PWM Motor 2
P9_12	GPIO_60	Enable ESCON 1
P8_18	GPIO_65	Enable ESCON 2
P9_42B(92)	eQEP0A	Encoder 1 – Chan A
P9_27	eQEP0B	Encoder 1 – Chan B
P8_12	eQEP2A	Encoder 2 – Chan A
P8_11	eQEP2B	Encoder 2 – Chan B
P9_17	SPI_CS	Slave selection
P9_18	SPI_MOSI	Master Out Slave In
P8_21	SPI_MISO	Master In Slave Out
P8_22	SPI_SCLK	SPI Clock Signal

Connections ESCON:
J1: Power	1	Alim -
	2	Alim +
J2: Motor	1	Motor +
	2	Motor -
J3:Hall Sensor	4	+5VDD Alim carte ADC
	5	GND Alim carte ADC
J4: Encoder	2	+ 5VDC (Encoder supply) – NOT CONNECTED
	3	GND
	6	Channel A
	8	Channel B
J5: Digital	1	PWM
	2	Enable
	5	GND

ESCON to BBB encoder cable:
(right to left while facing the connector)
2	Red	+ 5VDC (Encoder supply) – NOT CONNECTED
3	Orange	GND
6	Blue	Channel A
8	Green	Channel B

Encoder to BBB shielded cable:
Color	Stripe	Function
Red	Black	+5V – encoder power supply
Black	Red	GND
White	Black	Channel A
Green	Black	Channel B

SPI Protocol BBB ← → ADC
24 bits (8 write + 16 read)
Write in MOSI:
AIN1 : 0x9E
AIN2 : 0xDE
AIN3 : 0xAE
AIN4 : 0xEE
Read : 0x00
Read in MISO: First 9 bits are 0, next 12 are the data, last 3 are always 0.

Force sensors to hx711 (not used anymore):
E+	Red
E-	Black
S-	White
S+	Green

hx711 to BBB (not used anymore):
hx711	BBB
GND	Not connected (only one needed)
VCC	Not connected (only one needed)
DOUT	Force Sensor 1 SIG (IN) (cf table 1)
Cable soldered on PIN 15	+3.3 V
GND	GND
VCC	+3.3 V
SCK	Force Sensor 1 SCK (OUT) (cf table 1)